## Slide 1: Accumulators and Accumulator Circuits
From
“Fluid Power Circuits Explained”
By Bud Trinkel
Certified Fluid Power Engineer
HYDRA-PNEU CONSULTING, INC.
Newburgh, IN 47630-1517
812-853-3234
fluidpower1@hotmail.com

## Slide 2: Accumulators and Accumulator Circuits
Left mouse click or Enter for next slide
Backspace for previous slide
Right mouse click to pull up menu to GO anywhere in program
“Pause” key stops and starts animation
Left mouse click to return to start of section
Left mouse click to return to Agenda

## Slide 3: Accumulators and Accumulator Circuits You Will Learn
How the two most common accumulators are made and how they function plus a simple non- intrusive way to check pre-charge
Other accumulator types in cutaway and symbol
What the four common accumulator circuits are, how they are designed and how they operate
An unconventional circuit to use more of an accumulators stored energy

## Slide 4
Color Coding for Circuits
Working Fluid from Pump or Compressor
Return Fluid to Tank or Atmosphere
Suction or Intake Fluid, Drain Fluid
Flow Controlled Fluid
Reduced Pressure fluid, Pilot Pressure, Accumulator Pre-charge Pressure
Intensified Pressure Fluid, Load Induced Pressure Fluid
Inactive Fluid

## Slide 5: Agenda
Slides 6-29: Bladder and piston accumulator design and function plus two non-intrusive ways to check pre- charge
Slides 30-33: Other accumulator types
Slides 34-69: Supplementing pump flow
Slides 70-96: Make up for leakage
Slides 97-137: Absorb shock
Slides 138-152: Emergency power supply
Slides 153-183: Accumulator circuit to use more stored energy

## Slide 6: Two Most Common Accumulator Designs
Top Repairable Bladder
Floating Piston
Symbol
Spring Open Shutoff Poppet
Fill and Discharge Port
Nitrogen Fill Valve
Bladder
Piston
Gas Charge
Oil Space
Wear Band
Piston Seals
Most Responsive Type Accumulator
Best Accumulator For Maximum Fluid Storage
Slower response due to piston weight and seal friction

## Slide 7: Typical Accumulator Cycle Progression
Accumulators At Rest, Pump Off
Max. System Pressure 2,500 PSI Min. Working Pressure 1,500 PSI Pre-charge Pressure 1,275 PSI
Approximately 51 Cubic Inches of Stored Energy per 1 Gallon of Accumulator Volume
Symbol
0 PSI
0 PSI
From Pump
To System

## Slide 8: Typical Accumulator Cycle Progression
Pump On, System Full of Fluid
At PUMP ON, the circuit starts filling with fluid and system pressure suddenly jumps to nitrogen pre-charge pressure. Then pressure continues to build to maximum system pressure as the accumulator fills.
Symbol
1,275 PSI
1,275 PSI
From Pump
To System

## Slide 9: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
1,375 PSI
1,375 PSI
From Pump
To System

## Slide 10: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
1,475 PSI
1,475 PSI
From Pump
To System

## Slide 11: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
1,700 PSI
1,700 PSI
From Pump
To System

## Slide 12: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
1,900 PSI
1,900 PSI
From Pump
To System

## Slide 13: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
2,000 PSI
2,000 PSI
From Pump
To System

## Slide 14: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
2,150 PSI
2,150 PSI
From Pump
To System

## Slide 15: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
2,250 PSI
2,250 PSI
From Pump
To System

## Slide 16: Typical Accumulator Cycle Progression
Pump On, Accumulator Filling
Symbol
2,350 PSI
2,350 PSI
From Pump
To System

## Slide 17: Typical Accumulator Cycle Progression
Pump On, Accumulator Full
Symbol
2,500 PSI
2,500 PSI
From Pump
To System
The system is ready for a new cycle. A fixed volume pump is unloading at this time. A pressure compensated pump is compensated to no flow.

## Slide 18: Typical Accumulator Cycle Progression
Pump On, Accumulator Full
Symbol
2,500 PSI
2,500 PSI
From Pump
To System
When the cycle starts both accumulator and pump supply fluid for a fast approach from a small power unit.

## Slide 19: Typical Accumulator Cycle Progression
Pump and Accumulator Supplying Circuit
Symbol
2,350 PSI
From Pump
2,350 PSI
To System

## Slide 20: Typical Accumulator Cycle Progression
Symbol
2,250 PSI
2,250 PSI
From Pump
To System
Pump and Accumulator Supplying Circuit

## Slide 21: Typical Accumulator Cycle Progression
Symbol
2,150 PSI
2,150 PSI
From Pump
To System
Pump and Accumulator Supplying Circuit

## Slide 22: Typical Accumulator Cycle Progression
Symbol
2,000 PSI
2,000 PSI
From Pump
To System
Pump and Accumulator Supplying Circuit

## Slide 23: Typical Accumulator Cycle Progression
Symbol
1,900 PSI
1,900 PSI
From Pump
To System
Pump and Accumulator Supplying Circuit

## Slide 24: Typical Accumulator Cycle Progression
Symbol
1,700 PSI
1,700 PSI
From Pump
To System
Pump and Accumulator Supplying Circuit

## Slide 25: Typical Accumulator Cycle Progression
Symbol
1,500–1,600 PSI
1,500–1,600 PSI
To System
If all is working as designed the accumulator will never discharge completely during normal machine cycles. This keeps the bladder or piston from bottoming and being damaged
Cycle Complete Ready For Accumulator To Refill
From Pump

## Slide 26: Typical Accumulator Cycle Progression
Symbol
1,400 PSI
1,400 PSI
To System
All accumulator circuits must have a means of discharging all fluid at pump shut down. This dump system can be automatic or manual. Place conspicuous warning signs indicating stored energy possibility.
Pump Shut Down, Accumulator Draining to Tank
From Pump

## Slide 27: Typical Accumulator Cycle Progression
Symbol
1,300 PSI
1,300 PSI
To System
Pump Shut Down, Accumulator Draining to Tank
From Pump

## Slide 28: Typical Accumulator Cycle Progression
1,275 PSI
1,275 PSI
To System
As fluid discharges pressure continues to drop on the gauge at the outlet since it is reading fluid pressure. When all fluid is depleted---
Pump Shut Down, Accumulator Draining to Tank
From Pump
Symbol

## Slide 29: Typical Accumulator Cycle Progression
0 PSI
0 PSI
To System
When all fluid is depleted, gauge pressure suddenly falls to zero. Gauge pressure drops suddenly at pre-charge pressure.
Pump Shut Down, Accumulator Draining to Tank
From Pump
Symbol

## Slide 30: Other Accumulator Types
Symbol
Spring Loaded Piston
Fill and Discharge Port
Piston
Oil Space
Wear Band
Piston Seals
Spring
Piston Stroke Limiter Post
Has the same basic operating characteristic as a Gas Charged Piston Accumulator.
Has less stored energy and/or maximum pressure as the same size Gas Charged Piston Accumulator.
Never loses gas though springs weaken and stored energy capabilities lessen over life of spring.
Easy to determine piston seal leakage
Fairly slow response due to piston weight and seal friction.
Vent Port

## Slide 31: Other Accumulator Types
Symbol
Weight Loaded Ram or Piston
Discharge Port
Weight: Could be Concrete, Lead shot, Steel scrap, Water or other liquids, anything with weight.
Ram or Piston
These accumulators are large and bulky and are not usually found on small individual machines.
They are commonly seen in Rolling Mills and could be used in Central Hydraulic Systems.
This type accumulator does not have a pressure decrease as fluid discharges until the Ram or Piston hits bottom.
Some means of slowing the decent, mechanical or hydraulic, is usually provided in case of a line break.

## Slide 32: Other Accumulator Types
Non Separated
Symbol
Normally only found on older machines.
Must have an automatic or manual shut off to close the discharge line before all fluid if depleted.
Charged with nitrogen to maximum system pressure after filling to desired level with fluid.
Sight Glass
Nitrogen Fill Valve
Discharge Port
Nitrogen Gas
Nitrogen Gas

## Slide 33: Other Accumulator Types
Air Over Hydraulic
Symbol
This type Accumulator is similar to a Weight Loaded design. Pressure at the discharge port diminishes only a small amount as fluid is used.
It takes a lot less space than the Weight Loaded design and can be mounted in almost any position when required. Vertical is recommended
Air Port Usually 200-250 PSI with a Surge Tank to minimize pressure drop
Discharge Port
Breather Port
Air Piston
Ram
The area ratio between the Air Piston and the Ram times air pressure gives the hydraulic output pressure.

## Slide 34: Accumulator Isolation, Unloading and Dump Valves
Pilot to Close Check Valve
Cutaway
Accumulator Isolation, Unloading and Dump Valve for Fixed Volume Pumps
Symbol
Accumulator Isolation and Dump Valve for Pressure Compensated Pumps
Isolation Check Valve
Pump In
System
Accumulator
Tank Drain
Pump In
Accumulator
Tank Drain
System
System
Accumulator
Pump In
Isolation Check Valve
High Ratio Pilot to Close Check Valve
Tank
Pump In
Tank
Pilot Section
Adjusting Screw
Unloading Relief Valve
Unloading Relief Valve

## Slide 35: Accumulator to Supplement Pump Flow
At Rest Pump Off
Cycle Sequence: Extend 5 Seconds Hold 30 Seconds Retract 2 ½ Seconds Pause 20 Seconds Max. Pressure 2,000 PSI Min. Pr. 700–1,250 PSI Nitrogen Pre-charge Pressure 595 PSI
Symbol
A B
P T
PG1
0 PSI
Cutaway
Cutaway
PG2
0 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 36: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
700 PSI
Cutaway
Cutaway
PG2
700 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 37: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
830 PSI
Cutaway
Cutaway
PG2
830 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 38: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
960 PSI
Cutaway
Cutaway
PG2
960 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 39: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,090 PSI
Cutaway
Cutaway
PG2
1,090 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 40: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,220 PSI
Cutaway
Cutaway
PG2
1,220 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 41: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,350 PSI
Cutaway
Cutaway
PG2
1,350 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 42: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,480 PSI
Cutaway
Cutaway
PG2
1,480 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 43: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,610 PSI
Cutaway
Cutaway
PG2
1,610 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 44: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,740 PSI
Cutaway
Cutaway
PG2
1,740 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 45: Accumulator to Supplement Pump Flow
At Rest Pump Running Accumulator Filling
Symbol
A B
P T
PG1
1,870 PSI
Cutaway
Cutaway
PG2
1,870 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 46: Accumulator to Supplement Pump Flow
Accumulator Filled Just Before Unloading Pump
Symbol
A B
P T
PG1
2,000 PSI
Cutaway
PG2
2,000 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
Cutaway
Symbol
Set 2,000 PSI
When the system is at pressure the dump valve starts opening to send pump flow to tank and isolate the accumulator from the pump.

## Slide 47: Accumulator to Supplement Pump Flow
At Rest Pump Running, Accumulator Full, Pump Unloading
The Accumulator Dump Valve isolates the accumulator from the pump and tank and unloads the pump to tank at minimum pressure.
Symbol
A B
P T
PG1
0 PSI
Cutaway
Cutaway
PG2
2,000 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI

## Slide 48: Accumulator to Supplement Pump Flow
Cylinder Starting to Extend From Accumulator
Symbol
A B
P T
PG1
0 PSI
Cutaway
Cutaway
PG2
1,850 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
First flow to the cylinder is from the accumulator. Pressure must drop approximately 15% before the pump loads again. Cylinder speed is set by Meter In Needle Valve

## Slide 49: Accumulator to Supplement Pump Flow
Cylinder Extending From Accumulator and Pump
Symbol
A B
P T
PG1
150+ PSI
Cutaway
Cutaway
PG2
1,700 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
At approximately 1,700 PSI the Accumulator Dump Valve starts closing to force pump flow to the circuit.

## Slide 50: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
1,550- PSI
Cutaway
Cutaway
PG2
1,550 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Below 1,700 PSI the Accumulator Dump Valve closes to force all pump flow to the circuit. Both pump and accumulator flow are supplying the cylinder.
Cylinder Extending From Accumulator and Pump

## Slide 51: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
1,400 PSI
Cutaway
Cutaway
PG2
1,400 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Cylinder Extending From Accumulator and Pump

## Slide 52: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
1,250 PSI
Cutaway
Cutaway
PG2
1,250 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Cylinder Extending From Accumulator and Pump

## Slide 53: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
1,100 PSI
Cutaway
Cutaway
PG2
1,100 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Cylinder Extending From Accumulator and Pump

## Slide 54: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
950 PSI
Cutaway
Cutaway
PG2
950 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
700 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
When the cylinder makes work contact pressure builds, the pressure switch shifts to de-energize the directional valve extend solenoid.
Cylinder Just Reaching Pressure of 700 PSI

## Slide 55: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
700 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
When the directional valve centers the pilot operated check valve closes trapping fluid in the cylinder. The pump continues feeding the circuit and refilling the accumulator.
Cylinder at 700 PSI Accumulator Refilling
1,100 PSI
1,100 PSI

## Slide 56: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
700 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Cylinder at 700 PSI Accumulator Refilling
1,250 PSI
1,250 PSI

## Slide 57: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
700 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Cylinder at 700 PSI Accumulator Refilling
1,400 PSI
1,400 PSI

## Slide 58: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
700 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
Cylinder at 700 PSI Accumulator Refilling
1,550 PSI
1,550 PSI

## Slide 59: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
650 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
During the 30 second delay, minor leakage or bypass can cause a loss of pressure at the cylinder. When this happens the pressure switch---
Cylinder at 700 PSI Accumulator Refilling
1,700 PSI
1,700 PSI

## Slide 60: Accumulator to Supplement Pump Flow
Symbol
A B
P T
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
700 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
If this happens the pressure switch shift’s the directional valve to refill the cylinder back to set pressure and re-centers it after reaching set pressure.
Cylinder at 700 PSI Accumulator Refilling
1,850 PSI
1,850 PSI

## Slide 61: Accumulator to Supplement Pump Flow
Cutaway
Pressure Switch Set 700 PSI
PG3
700 PSI
Counter Balance Valve
Platen
2,000 PSI
Symbol
A B
P T
PG1
PG2
2,000 PSI
Pilot Operated Check Valve
Meter In Needle Valve
Cutaway
Symbol
Set 2,000 PSI
Accumulator Filled Just Before Unloading Pump
When the system is at pressure the dump valve starts opening to send pump flow to tank and isolate the accumulator from the pump.

## Slide 62: Accumulator to Supplement Pump Flow
Cutaway
Pressure Switch Set 700 PSI
PG3
700 PSI
Counter Balance Valve
Platen
0 PSI
At Rest Pump Running Accumulator Full, Pump Unloading
Symbol
A B
P T
PG1
Cutaway
PG2
2,000 PSI
Pilot Operated Check Valve
Meter In Needle Valve
Symbol
Set 2,000 PSI
The Accumulator Dump Valve isolates the accumulator from the pump and tank and unloads the pump to tank at minimum pressure.

## Slide 63: Accumulator to Supplement Pump Flow
Cylinder Starting to Retract From Accumulator
Symbol
A B
P T
PG1
0 PSI
Cutaway
Cutaway
PG2
1,850 PSI
Pressure Switch Set 700 PSI
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Symbol
Platen
Set 2,000 PSI
First flow to the cylinder is from the accumulator. Pressure must drop approximately 15% before the pump loads again. Cylinder speed is set by Meter In Needle Valve

## Slide 64: Accumulator to Supplement Pump Flow
Cylinder Retracting From Accumulator and Pump
Symbol
PG1
150+ PSI
Cutaway
Cutaway
PG2
1,700 PSI
Pressure Switch Set 700 PSI
Meter In Needle Valve
Symbol
Set 2,000 PSI
At approximately 1,700 PSI the Accumulator Dump Valve starts closing to force pump flow to the circuit.
A B
P T
Pilot Operated Check Valve
PG3
0 PSI
Counter Balance Valve
Platen

## Slide 65: Accumulator to Supplement Pump Flow
Symbol
PG1
1,550- PSI
Cutaway
Cutaway
PG2
1,550 PSI
Pressure Switch Set 700 PSI
Meter In Needle Valve
Symbol
Set 2,000 PSI
Below 1,700 PSI the Accumulator Dump Valve closes to force all pump flow to the circuit. Both pump and accumulator flow are supplying the cylinder.
Cylinder Retracting From Accumulator and Pump
A B
P T
Pilot Operated Check Valve
PG3
0 PSI
Counter Balance Valve
Platen

## Slide 66: Accumulator to Supplement Pump Flow
Symbol
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Meter In Needle Valve
Symbol
Set 2,000 PSI
Cylinder Just Fully Retracted Accumulator Refilling
1,700 PSI
1,700 PSI
A B
P T
Pilot Operated Check Valve
PG3
0 PSI
Counter Balance Valve
Platen

## Slide 67: Accumulator to Supplement Pump Flow
Symbol
PG1
Cutaway
Cutaway
PG2
Pressure Switch Set 700 PSI
Meter In Needle Valve
Symbol
Set 2,000 PSI
1,850 PSI
1,850 PSI
Cylinder Fully Retracted Accumulator Refilling
A B
P T
Pilot Operated Check Valve
PG3
0 PSI
Counter Balance Valve
Platen

## Slide 68: Accumulator to Supplement Pump Flow
Cutaway
Pressure Switch Set 700 PSI
2,000 PSI
Symbol
PG1
PG2
2,000 PSI
Meter In Needle Valve
Cutaway
Symbol
Set 2,000 PSI
Accumulator Filled Just Before Unloading Pump
When the system is at pressure the dump valve starts opening to send pump flow to tank and isolate the accumulator from the pump.
A B
P T
Pilot Operated Check Valve
PG3
0 PSI
Counter Balance Valve
Platen

## Slide 69: Accumulator to Supplement Pump Flow
Cutaway
Pressure Switch Set 700 PSI
0 PSI
At Rest Pump Running, Accumulator Full, Pump Unloading
Symbol
PG1
Cutaway
PG2
2,000 PSI
Meter In Needle Valve
Symbol
Set 2,000 PSI
The Accumulator Dump Valve isolates the accumulator from the pump and tank and unloads the pump to tank at minimum pressure.
A B
P T
Pilot Operated Check Valve
PG3
0 PSI
Counter Balance Valve
Platen

## Slide 70: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
At Rest Pump Running
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Cycle Sequence: Extend 10 Seconds Hold 50 Seconds Retract 5 Seconds Max. Pressure 2,000 PSI Min. Pressure 1,400 PSI Nitrogen Pre-charge Pressure 1,000 PSI
PG1
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI
0 PSI

## Slide 71: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
When the directional valve shifts the press cylinder starts extending at whatever pressure it takes to move it.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 72: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 73: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 74: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 75: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 76: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 77: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 78: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 79: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
175 PSI
175 PSI

## Slide 80: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,000 PSI
1,000 PSI
At work contact pressure quickly builds to pre-charge pressure and continues to climb

## Slide 81: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder Extending
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,150 PSI
1,150 PSI
At work contact pressure quickly builds to pre-charge pressure and continues to climb to Pressure Switch setting of 1,500 PSI

## Slide 82: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Cylinder on Work Building Tonnage
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,300 PSI
1,300 PSI

## Slide 83: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,450 PSI
1,450 PSI
Cylinder on Work Building Tonnage

## Slide 84: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,500 PSI
1,500 PSI
After reaching Pressure Switch setting of 1,500 PSI the directional valve
Cylinder on Work at Tonnage

## Slide 85: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,500 PSI
1,500 PSI
After reaching Pressure Switch setting of 1,500 PSI the directional valve centers blocking fluid in the cylinder cap end and unloading the pump.
Any bypass or leaks can now be made up from stored energy in the Accumulator
Cylinder on Work at Tonnage

## Slide 86: Accumulator to Make Up for Leakage
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Inlet Maximum 2,000 PSI
Small Bladder Accumulator. Usually under 1 ½ Gallon.
Any bypass or leaks can now be made up from stored energy in the Accumulator
Cylinder on Work, Tonnage Deteriorating
PG2
Cutaway
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
PG1
1,400 PSI
1,400 PSI

## Slide 87: Accumulator to Make Up for Leakage
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Inlet Maximum 2,000 PSI
Small Bladder Accumulator. Usually under 1 ½ Gallon.
At 1,400 PSI the Pressure Switch makes and shifts the directional valve to send pump flow to refill the Accumulator. Then the directional valve---
Cylinder on Work, Tonnage Deteriorated to 1,400 PSI
PG2
Cutaway
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
PG1
1,400 PSI
1,400 PSI

## Slide 88: Accumulator to Make Up for Leakage
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Inlet Maximum 2,000 PSI
Small Bladder Accumulator. Usually under 1 ½ Gallon.
to refill the Accumulator. Then the directional valve returns to center to block fluid in the cylinder cap end and unload the pump.
Cylinder on Work, Tonnage Deteriorated to 1,400 PSI
PG2
Cutaway
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
PG1
1,400 PSI
1,400 PSI

## Slide 89: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,500 PSI
1,500 PSI
This sequence automatically repeats as often as required while the parts are clamped.
Cylinder on Work at Tonnage

## Slide 90: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
PG1
1,500 PSI
0 PSI
When parts are through the directional valve shifts to send cap end fluid to tank and pump flow to the rod end to return it to home position.
The Accumulator slowly discharges its stored energy during this part of the cycle.
Cylinder Unclamping and Retracting

## Slide 91: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI
Cylinder Unclamping and Retracting
Symbol
PG1
1,450 PSI

## Slide 92: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI
Cylinder Unclamping and Retracting
Symbol
PG1
1,300 PSI

## Slide 93: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI
Cylinder Unclamping and Retracting
Symbol
PG1
1,150 PSI

## Slide 94: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI
Cylinder Unclamping and Retracting
Symbol
PG1
1,000 PSI

## Slide 95: Accumulator to Make Up for Leakage
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI
Cylinder Unclamping and Retracting
Symbol
PG1
0 PSI

## Slide 96: Accumulator to Make Up for Leakage
Cylinder Stopped
0 PSI
When cylinder fully retracts the directional valve centers to stop it and unload the pump.
A manual drain on the Accumulator outlet can be opened to relieve any stored energy at shutdown.
PG2
A
B
P
T
Pressure Switch Set 1,500 PSI Shift 1,400 PSI Reset
Symbol
Cutaway
Inlet Maximum 2,000 PSI
Meter Out Flow Control Set to discharge accumulator in 4 seconds maximum.
PG1
Small Bladder Accumulator. Usually under 1 ½ Gallon.
0 PSI

## Slide 97: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (Without Accumulator)
3,000 PSI
Pressure compensated piston pumps change volume in relation to system requirements through Swash Plate angle changes. As pressure drops Swash Plate angle increases and gives increased flow. When pressure raises to near compensator setting flow lessens and finally stops as shown here.
PG1
A B
P T
0 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
No Flow
Full Flow
Swash Plate

## Slide 98: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
2,800 PSI
When the directional valve shifts to extend the cylinder, pressure is maximum but flow is zero. Some fluid goes to the actuator and pressure drops in the first few milliseconds. The Swash Plate starts changing angle to give flow but the actuator has not started moving yet. Pressure continues to drop and Swash Plate angle
PG1
A B
P T
1+ GPM
Swash Plate
Set Compensator 3,000 PSI
Flow Starting
Cutaway

## Slide 99: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
700- PSI
Pressure continues to drop and Swash Plate angle continues to increase until pump is at full flow and pressure is whatever it takes to move the cylinder.
It takes approximately .05 to .10 seconds for the pump to come on full stroke.
PG1
A B
P T
50 GPM
Swash Plate
Set Compensator 3,000 PSI
Flow Increasing
Cutaway

## Slide 100: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 101: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 102: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 103: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 104: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 105: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 106: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 107: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150- PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 108: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 109: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Set Compensator 3,000 PSI
Full Flow
Cutaway

## Slide 110: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
750 PSI
PG1
A B
P T
60 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Full Flow
At work contact no more flow is needed so pressure starts to climb due to flow resistance.

## Slide 111: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
1,700 PSI
PG1
A B
P T
60 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Full Flow
However, the pump is still at full flow and will not start to compensate to zero flow until pressure reaches approximately 2,800-2,900 PSI. This takes from .06 to .15 seconds so an extra 80-1203” of fluid is pumped into a dead end circuit.

## Slide 112: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
2,850 PSI
PG1
A B
P T
40 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Reducing Flow
At approximately 2,850 PSI the pump compensator reaches high enough pressure to start reducing flow quickly.

## Slide 113: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
5,900 PSI
PG1
A B
P T
25 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Reducing Flow
At 3,000 PSI the pump reaches compensator setting and flow goes to zero.

## Slide 114: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (Without Accumulator)
12,000 PSI
PG1
A B
P T
0 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Extra fluid pushed into the circuit during pump compensation gives a pressure spike. Pressure spikes during these end of stroke or valve centering situations can reach 3-5 times compensator setting causing damage to the pump, valves and piping.
No Flow

## Slide 115: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
150 PSI
PG1
A B
P T
60 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Many circuit designers add a Relief Valve in the pump line since they respond faster to pressure spikes. The Relief Valve is set 100-150 PSI higher than the pump compensator so it only dumps when pressure exceeds compensator setting plus.
Now the end of stroke looks like this---
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response
Full Flow

## Slide 116: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
750 PSI
PG1
A B
P T
60 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Full Flow
At work contact no more flow is needed so pressure starts to climb due to flow resistance.
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response

## Slide 117: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
1,700 PSI
PG1
A B
P T
40 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Full Flow
However, the pump is still at full flow and will not start to compensate to zero flow until pressure reaches approximately 2,800-2,900 PSI. This takes from .06 to .15 seconds so an extra 80-1203” of fluid is pumped into a dead end circuit.
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response

## Slide 118: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
2,850 PSI
PG1
A B
P T
25 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Reducing Flow
At approximately 2,850 PSI the pump compensator reaches high enough pressure to start reducing flow quickly.
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response

## Slide 119: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
3,500 PSI
PG1
A B
P T
12 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Reducing Flow
At 3,000 PSI the pump reaches compensator setting and flow continues to decrease while pressure increases.
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response

## Slide 120: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
6,000 PSI
PG1
A B
P T
5 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
Extra fluid pushed into the circuit during pump compensation gives a pressure spike. Pressure spikes during these end of stroke or valve centering situations can reach 1 ½ to 2 times Relief Valve setting causing damage to the pump, valves and piping.
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response
Reducing Flow

## Slide 121: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump Cylinder Extending (With Relief Valve )
3,000 PSI
PG1
A B
P T
0 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
At No Flow pressure drops to 3,000 PSI and the Relief Valve closes to stop flow to tank.
A better circuit follows.
Set 3,150 PSI
A Direct Acting Relief Valve works best in this situation due to faster response
No Flow

## Slide 122: Accumulator to Absorb Shock
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
3,000 PSI
With the circuit at rest the accumulator fills and pump flow goes to No Flow as shown. There is a ready supply of fluid at 3,000 PSI stored in the accumulator.
The accumulator is a 2 ½ gallon size pre-charged to 1,800 PSI The Sequence Valve is set at 2,000 PSI so there is approximately 100 cubic inches of stored energy.
Symbol
Cutaway
PG1
A B
P T
0 GPM
Swash Plate
Cutaway
Set Compensator 3,000 PSI
No Flow
Sequence Valve Set 2,000 PSI
PG2
3,000 PSI

## Slide 123: Accumulator to Absorb Shock
2,850 PSI
When the directional valve shifts to extend the cylinder, pressure is maximum but pump flow is zero. Fluid from the accumulator goes to the actuator to start it moving immediately and pressure drops at the pump outlet. The Swash Plate starts changing angle to give flow. Pressure continues to drop and Swash Plate angle
PG1
A B
P T
1+ GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Flow Starting
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Sequence Valve Set 2,000 PSI
Symbol
Cutaway
PG2
2,850 PSI

## Slide 124: Accumulator to Absorb Shock
Pressure continues to drop and Swash Plate angle continues to increase until pump is at full flow and pressure is whatever it takes to move the cylinder.
It takes approximately .05 to .10 seconds for the pump to come on full stroke.
700 PSI
PG1
A B
P T
50 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Flow Increasing
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Sequence Valve Set 2,000 PSI
Symbol
Cutaway
PG2
2,000 PSI

## Slide 125: Accumulator to Absorb Shock
Pressure continues to drop and Swash Plate angle continues to increase until pump is at full flow and pressure is whatever it takes to move the cylinder.
Accumulator flow is stopped at the Sequence Valve so it does not bottom each cycle.
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 126: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 127: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 128: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 129: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 130: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 131: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 132: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 133: Accumulator to Absorb Shock
150 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI
At work contact no more flow is needed so pressure starts to climb due to flow resistance.

## Slide 134: Accumulator to Absorb Shock
However, the pump is still at full flow and will not start to compensate to zero flow until pressure reaches approximately 2,800-2,900 PSI. This takes from .06 to .15 seconds so an extra 80-1203” of fluid is pumped into the circuit.
1,500 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 135: Accumulator to Absorb Shock
With an accumulator in the circuit pump flow can start filling it at about 2,000-2,100 PSI. This allows the pump to see less stress since there is a flow path at a pressure less than its compensator setting.
2,100 PSI
PG1
A B
P T
60 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Full Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,000 PSI

## Slide 136: Accumulator to Absorb Shock
At approximately 2,850 PSI the pump compensator reaches high enough pressure to start reducing flow quickly.
While the pump goes to no flow the accumulator takes in excess fluid with minimum pressure increase.
2,850 PSI
PG1
A B
P T
40 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Reducing Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
2,850 PSI

## Slide 137: Accumulator to Absorb Shock
At 3,000 PSI the pump reaches compensator setting and flow goes to zero.
3,000 PSI
PG1
A B
P T
20 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
Reducing Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
3,000 PSI

## Slide 138: Accumulator to Absorb Shock
Extra fluid pushed into the circuit while the pump is compensating goes into the accumulator and pressure increases only a little above compensator setting.
3,500 PSI
PG1
A B
P T
0 GPM
Set Compensator 3,000 PSI
Swash Plate
Cutaway
No Flow
Sequence Valve Set 2,000 PSI
High Volume (60 GPM) Pressure Compensated Pump At Rest Pump Running (With Accumulator)
Symbol
Cutaway
PG2
3,500 PSI

## Slide 139: Accumulator for Emergency Power Supply
PG2
Symbol
Cutaway
0 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure At Rest Pump Off
A
B
P
T
Slide Gate
Maximum Pressure 2,500 PSI Minimum Pressure 1,500 PSI Pre-charge Pressure 1,275 PSI
Wire Solenoids “c1” and “c2” in parallel with pump motor starter
“a”
“b”
“c1”
“c2”
0 PSI
PG1
Set Compensator 2,500 PSI

## Slide 140: Accumulator for Emergency Power Supply
1,575 PSI
PG2
Symbol
Cutaway
PG1
1,575 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure At Rest Pump Running, Accumulator Filling
A
B
P
T
Slide Gate
Maximum Pressure 2,500 PSI Minimum Pressure 1,500 PSI Pre-charge Pressure 1,275 PSI
Wire Solenoids “c1” and “c2” in parallel with pump motor starter
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 141: Accumulator for Emergency Power Supply
1,875 PSI
PG2
Symbol
Cutaway
PG1
1,875 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure At Rest Pump Running, Accumulator Filling
A
B
P
T
Slide Gate
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 142: Accumulator for Emergency Power Supply
2,175 PSI
PG2
Symbol
Cutaway
PG1
2,175 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure At Rest Pump Running, Accumulator Filling
A
B
P
T
Slide Gate
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 143: Accumulator for Emergency Power Supply
2,500 PSI
PG2
Symbol
Cutaway
PG1
2,500 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure At Rest Pump Running, Accumulator Filling
A
B
P
T
Slide Gate
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 144: Accumulator for Emergency Power Supply
1,250 PSI
PG2
Symbol
Cutaway
PG1
2,500 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure Accumulator Full, Slide Gate Opening
A
B
P
T
Slide Gate
After the accumulator fills the Slide Gate can be cycled at will when power is on.
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 145: Accumulator for Emergency Power Supply
1,250 PSI
PG2
Symbol
Cutaway
PG1
2,500 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure Accumulator Full, Slide Gate Opening
A
B
P
T
Slide Gate
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 146: Accumulator for Emergency Power Supply
950 PSI
PG2
Symbol
Cutaway
PG1
2,500 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure Accumulator Full, Slide Gate Opening
A
B
P
T
Slide Gate
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 147: Accumulator for Emergency Power Supply
950 PSI
PG2
Symbol
Cutaway
PG1
2,500 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure Accumulator Full, Slide Gate Opening
A
B
P
T
Slide Gate
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”

## Slide 148: Accumulator for Emergency Power Supply
2,500 PSI
PG2
Symbol
Cutaway
PG1
2,500 PSI
Hopper
Slide Gate Closing Circuit in Case of Power Failure Accumulator Full, Slide Gate Open
A
B
P
T
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”
Slide Gate
If electric power fails while the Slide Gate is open it will automatically close without operator intervention
Guard any pinch points at the gate and place warning signs at the Slide Gate location to warn of possible uncontrolled movement!

## Slide 149: Accumulator for Emergency Power Supply
0 PSI
PG1
Hopper
Slide Gate Closing Circuit in Case of Power Failure Slide Gate Closing at Power Failure
A
B
P
T
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”
Slide Gate
When power fails the pump stops and solenoids “c1” and ”c2” de-energize.
Guard any pinch points at the gate and place warning signs at the Slide Gate location to warn of possible uncontrolled movement!
PG2
Symbol
Cutaway
2,175 PSI

## Slide 150: Accumulator for Emergency Power Supply
0 PSI
PG1
Hopper
Slide Gate Closing Circuit in Case of Power Failure Slide Gate Closing at Power Failure
A
B
P
T
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”
Slide Gate
PG2
Symbol
Cutaway
1,875 PSI
The Slide Gate automatically closes from stored energy in the Accumulator.
Guard any pinch points at the gate and place warning signs at the Slide Gate location to warn of possible uncontrolled movement!

## Slide 151: Accumulator for Emergency Power Supply
0 PSI
PG1
Hopper
Slide Gate Closing Circuit in Case of Power Failure Slide Gate Closing at Power Failure
A
B
P
T
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”
Slide Gate
PG2
Symbol
Cutaway
1,875 PSI
The Slide Gate automatically closes from stored energy in the Accumulator.
Guard any pinch points at the gate and place warning signs at the Slide Gate location to warn of possible uncontrolled movement!

## Slide 152: Accumulator for Emergency Power Supply
0 PSI
PG1
Hopper
Slide Gate Closing Circuit in Case of Power Failure Slide Gate Closing at Power Failure
A
B
P
T
Set Compensator 2,500 PSI
“a”
“b”
“c1”
“c2”
Slide Gate
Size accumulator so gate is fully closed before accumulator discharges all fluid and/or falls below minimum closing pressure.
Guard any pinch points at the gate and place warning signs at the Slide Gate location to warn of possible uncontrolled movement!
PG2
Symbol
Cutaway
1,575 PSI

## Slide 153: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Off
Symbol
A B
P T
Cutaway
PG2
0 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
Cycle Sequence: Extend 5 Seconds Hold 30 Seconds Retract 2 ½ Seconds Pause 20 Seconds Max. Pressure 2,500 PSI Min. Pr. 700–1,250 PSI Nitrogen Pre-charge Pressure 400 PSI
PG1
0 PSI

## Slide 154: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
400 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
400 PSI

## Slide 155: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
610 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
610 PSI

## Slide 156: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
820 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
820 PSI

## Slide 157: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
1,030 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
1,030 PSI

## Slide 158: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
1,260 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
1,260 PSI

## Slide 159: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
1,470 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
1,470 PSI

## Slide 160: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
1,680 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
1,680 PSI

## Slide 161: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
1,890 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
1,890 PSI

## Slide 162: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
2,100 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
2,100 PSI

## Slide 163: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Filling
Symbol
A B
P T
Cutaway
PG2
2,310 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
2,310 PSI

## Slide 164: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Full
Symbol
A B
P T
Cutaway
PG2
2,500 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
0 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
2,500 PSI
Energizing solenoid “a” of the 4-Way directional valve and solenoid “c” of the 2-Way directional valve starts the cylinder extending fast with the accumulator and the pump.

## Slide 165: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
2,200 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
150 PSI

## Slide 166: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
1,900 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
150 PSI

## Slide 167: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
1,600 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
150 PSI

## Slide 168: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
1,300 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
150 PSI

## Slide 169: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
1,000 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
150 PSI

## Slide 170: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
700 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
150 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
150 PSI

## Slide 171: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
500 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
1,500 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
1,500 PSI
At work contact pressure starts to build in the cylinder cap end forcing the check valve from the accumulator to close. Pump flow now goes directly to the cylinder cap end and starts building tonnage.

## Slide 172: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
Symbol
A B
P T
Cutaway
PG2
500 PSI
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
2,200 PSI
When pressure in the cap end of the cylinder reaches pressure switch setting the 4-Way directional control valve centers and the 2-Way valve returns to the open position. This traps fluid in the cylinder cap end and allows pump flow to go to the accumulator.

## Slide 173: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
820 PSI
This traps fluid in the cylinder cap end and allows pump flow to go to the accumulator. The accumulator fills until pressure reaches pump compensator setting
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
820 PSI

## Slide 174: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
1,030 PSI
1,030 PSI

## Slide 175: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
1,260 PSI
1,260 PSI

## Slide 176: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
1,470 PSI
1,470 PSI
If pressure drops below the minimum pressure switch setting the 2-Way and 4-Way directional valves shift to send pump flow to the cylinder and return pressure to pressure switch setting.

## Slide 177: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder Extending From Pump and Accumulator
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,100 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
2,100 PSI
1,470 PSI

## Slide 178: A Pump Supplementing Circuit for Using More of the Stored Energy
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
2,200 PSI
When pressure in the cap end of the cylinder reaches pressure switch setting the 4-Way directional control valve centers and the 2-Way valve returns to the open position . This traps fluid in the cylinder cap end and allows pump flow to go to the accumulator.
1,470 PSI

## Slide 179: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
1,680 PSI
1,680 PSI

## Slide 180: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
1,890 PSI
1,890 PSI

## Slide 181: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
2,100 PSI
2,100 PSI

## Slide 182: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
Rapid Approach and Clamp Operation With Dwell Cylinder at Tonnage and Accumulator Refilling
PG2
2,310 PSI
2,310 PSI

## Slide 183: A Pump Supplementing Circuit for Using More of the Stored Energy
Symbol
A B
P T
Cutaway
PG2
Pressure Switch Set for maximum force
Pilot Operated Check Valve
Meter In Needle Valve
PG3
2,200 PSI
Counter Balance Valve
Platen
“a”
“b”
“c”
Set Compensator 2,500 PSI
Wire in parallel with “a” and “b” solenoids
PG1
PG2
2,500 PSI
2,500 PSI
Rapid Approach and Clamp Operation With Dwell At Rest Pump Running, Accumulator Full
The same action from the accumulator takes place on the retract stroke. This circuit gives maximum volume from the accumulator and fast tonnage at work contact
Always use a Piston type accumulator in this circuit.

## Slide 184: “Fluid Power Circuits Explained”
This information was taken from
“Fluid Power Circuits Explained”
It covers these and other ways to Use Accumulators in Fluid Power circuits
It also gives details on how to check pre-charge pressure without invading the fill valve.

## Slide 185: For More Information on Regeneration and Many Other Fluid Power Circuits See “Fluid Power Circuits Explained” by the Author of this Presentation
Table of Contents from “Fluid Power Circuits Explained”
1. Accumulator Circuits 13. Intensifier Circuits
2. Air Logic Valve Circuits 14. Proportional Control Valve Circuits
3. Air-Oil Circuits 15. Pump Circuits
4. Cartridge Valve Circuits 16. Reducing Valve Circuits
5. Counter Balance Valve Circuits 17. Regeneration Circuits
6. Cylinder Circuits 18. Relief Valve Circuits
7. Decompression Circuits 19. Rotary Actuator Circuits
8. Directional Control Valve Circuits 20. Sequence Valve Circuits
9. Filter Circuits 21. Servo Control Valve Circuits
10. Flow Control Circuits 22. Synchronizing Circuits
11. Flow Divider Circuits 23. Sample Actual Circuits
12. Fluid Motor Circuits

## Slide 186: “Fluid Power Circuits Explained”
The book is in schematic format so you need to be familiar with Fluid Power symbols to understand the circuits.
· The book contains 375 pages of basic pneumatic and hydraulic circuits shown in schematic form with an explanation of their function. It is in a convenient 3-ring binder format.
· There are 22 sections covering Accumulators, Air Logics, Air-Oil Systems, Cartridge valves, Counter Balance Valves, Cylinders, De-Compression, Directional Controls, Filters, Flow Dividers, Intensifiers, Proportional Valves, Pumps, Reducing Valves, Regeneration, Relief Valves, Rotary Actuators, Sequence Valves, Servo Controls and Synchronizing Circuits. There is also a section with some actual operating circuits with explanations.
· Most circuits show what happens when the valves and actuators cycle. A detailed explanation of the schematic explains cycle progress and possible problem areas.
List price is $105.00 plus $7.95 S&H for shipments in the continental U.S. All other countries will be billed actual postage/shipping cost for the requested method. Indiana residents add 5% Sales Tax.
Send a check or money order to: HYDRA-PNEU CONSULTING, INC.
726 Outer Gray Street
Newburgh, IN 47630-1517