## Slide 1: Air Logic Circuits
From
“Fluid Power Circuits Explained”
By Bud Trinkel
Certified Fluid Power Engineer
HYDRA-PNEU CONSULTING, INC.
Newburgh, IN 47630-1517
812-853-3234
fluidpower1@hotmail.com

## Slide 2: Air Logic Circuits
Left mouse click or Enter for next slide
Backspace for previous slide
Right mouse click to pull up menu to GO anywhere in program
“Pause” key stops and starts animation
Left mouse click to return to start of section
Left mouse click to return to Agenda

## Slide 3: Learn About Air Logic Components and Their Functions
Design and operation of Air Logic valves in cutaway and schematic format using ANSI symbols for Air Logic controls and Graphic ISO symbols
See examples of each component in an operating circuit in cutaway and schematic format
See how actual circuits might be designed and how they function
Learn about Sequencer Modules that simplify circuit design and trouble shooting

## Slide 4: Where to use Air Logic Controls
Replace Electric or Electronic Controls and the safety concerns they present in wet or dusty atmospheres or in explosion hazard areas.
On simple single function machines where an Anti-Tie Down start for safety and a return signal at work end would require adding electric controls and service
On multi function machines that need a controlled sequence of events but have no other need of electric power.
To eliminate the need for two craft’s, Electrical and Mechanical, when a machine needs maintenance.

## Slide 5
Color Coding for Circuits
Working Fluid from Pump or Compressor
Return Fluid to Tank or Atmosphere
Suction or Intake Fluid, Drain Fluid
Flow Controlled Fluid
Reduced Pressure fluid, Pilot Pressure, Accumulator Pre-charge Pressure
Intensified Pressure Fluid, Load Induced Pressure Fluid
Inactive Fluid

## Slide 6: Agenda
Slides 7-117: Air Logic components design and function in typical circuits
Slides 118-132: Other available Air Logic components and how they function
Slides 133-151: Typical Anti-Tie Down Air Logic Circuit
Slides 152-194: Programmable Air Logic Sequencer Modules and circuit design

## Slide 7
Air Logic “OR” Element
Passive “OR” Element
“OR” Elements give an Output when there is an Input.
The Output of passive “OR” Elements is always the highest pressure Input.
ISO 1219–1 Symbol
Cutaway
Output
A B
Output
A B
A B Output
Input at “A” only
Input at “B” only
Input at
“A” AND “B”
A B
50 PSI 90 PSI
90 PSI
ANSI B93-38 1976 Symbol
A B
A B Output
A B 50 PSI Output 90 PSI

## Slide 8
Air Logic “OR” Element Application
“OR” Element Operating a Cylinder From Any of Four Different Limit Valves
Cutaway
ANSI B93-38 1976 Symbol
ISO 1219–1 Symbol
LV1
LV2
LV3
LV4
LV1
LV1
LV2
LV2
LV3
LV3
LV4
LV4
60 PSI
80 PSI
30 PSI
40 PSI
30 PSI-80 PSI

## Slide 9: Some “OR” Air Logic Examples

## Slide 10
Air Logic “AND” Element
Passive “AND” Element
“AND” Elements require two Inputs to have an Output.
The Output of passive “AND” Elements is always the lowest pressure Input.
ISO 1219–1 Symbol
Cutaway
Output
A B
Output
A B
A Output B
Input at “A” only
A Output B
Input at “B” only
A B
A 50 PSI Output B
50 PSI 90 PSI
Input at
“A” AND “B”
A B
50 PSI 90 PSI
50 PSI
ANSI B93-38 1976 Symbol

## Slide 11
Air Logic “AND” Element Application
“AND” Element Operating a Cylinder After Four Different Limit Valves Are Activated
Cutaway
ANSI B93-38 1976 Symbol
ISO 1219–1 Symbol
LV1
LV2
LV3
LV4
LV4
LV4
LV3
LV3
LV2
LV2
LV1
LV1
60 PSI
80 PSI
30 PSI
40 PSI
30 PSI Max.

## Slide 12
A B Output 15 PSI 90 PSI
Air Logic “YES” Element
“YES” Element (Active AND Element)
These elements are called “AND” by some suppliers and “YES” by others. Unlike a passive “AND” element the Output always comes from the same port so this element can act as a signal amplifier
“YES” Elements require two Inputs to have an Output.
The Output of active “AND” Elements is always the Input at “B”.
ISO 1219–1 Symbol
Cutaway
Output
A B
Output
A B
A B Output
Input at “A” only
A B Output
Input at “B” only
Input at
“A” AND “B”
A B
15 PSI 90 PSI
90 PSI
ANSI B93-38 1976 Symbol
A B
Exhaust
Exhaust
Exhaust
Poppet area ratio is approximately 10:1 from “B” port side to diaphragm side

## Slide 13
Air Logic “YES” Element Application
“YES” Element Amplifying a Low Pressure Pilot Signal
Cutaway
ANSI B93-38 1976 Symbol
ISO 1219–1 Symbol
LV1
LV2
LV3
LV4
LV4
LV4
LV3
LV3
LV2
LV2
LV1
LV1
60 PSI
80 PSI
20 PSI
40 PSI
20 PSI 80 PSI
80 PSI
80 PSI

## Slide 14
A B Output
Air Logic “NOT” Element
“NOT” Element
These elements are Normally Open Three-Way valves that can pass or stop an Input.
They are normally passing.
The Output of a “NOT” Elements is always the Input at “B”.
ISO 1219–1 Symbol
Cutaway
Output
Output
A B
A B Output
Input at “A” only
Input at “B” only
A B Output
50 PSI 80 PSI
Input at
“A” AND “B”
A B
50 PSI 80 PSI
Exhausting
ANSI B93-38 1976 Symbol
A B
Poppet area ratio is approximately 10:1 from “B” port side to diaphragm side
Exhaust
Exhaust
Exhaust
Supply or Input
A
B

## Slide 15
Air Logic “NOT” Element Application
“NOT” Element Controlling a Cylinder Operation Cylinder Extending
Cutaway
ANSI B93-38 1976 Symbol
ISO 1219–1 Symbol
LV1
“This”
LV3
“OR” “This”
LV2
“NOT” This
LV1
LV2
LV3
LV1
LV3
LV2

## Slide 16
Air Logic “NOT” Element Application
“NOT” Element Controlling a Cylinder Operation Cylinder Stopped and Retracting
Cutaway
ANSI B93-38 1976 Symbol
ISO 1219–1 Symbol
LV1
“This”
LV3
“OR” “This”
LV2
“NOT” This
LV1
LV2
LV3
LV1
LV3
LV2

## Slide 17
ISO 1219–1 Symbol
Cutaway
Output
Output
A B
A B Output
Input at “A” only
A B Output
Input at “B” only
A B Output
50 PSI 80 PSI
Input at
“A” AND “B”
A B
50 PSI 80 PSI
Exhausting
A B
Poppet area ratio is approximately 20:1 from “B” port side to diaphragm side
Exhaust
Exhaust
Exhaust
Supply or Input
A
B
These elements are the same as a “NOT” element in function but have a higher ratio from “B” port side to to the diaphragm side. This means a low pressure at “A” port can block a high pressure at “B” port.
Manufacturers Symbol
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element

## Slide 18
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Circuit At Rest, Air On
Start Valve
Symbol Format

## Slide 19
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 20
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 21
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 22
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 23
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 24
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 25
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 26
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 27
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Start Valve Shifted, Cylinder Extending
Start Valve
Symbol Format

## Slide 28
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder at End of Stroke, Rod Pressure Dropping to Zero
Start Valve

## Slide 29
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder at End of Stroke, Rod Pressure Zero, Directional Valve Shifting
Start Valve

## Slide 30
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 31
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 32
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 33
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 34
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 35
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 36
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 37
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 38
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 39
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder Retracting
Start Valve

## Slide 40
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder at End of Stroke, Cap Pressure Dropping to Zero
Start Valve

## Slide 41
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Symbol Format
Cutaway Format
Cylinder at End of Stroke, Cap Pressure Zero, Directional Valve Shifting
Start Valve

## Slide 42
Air Logic “INHIBITOR” Element
“PRESSURE DECAY SENSOR” Element Reciprocating Circuit
Cutaway Format
Repeat Reciprocation Until Start Valve is Closed. Cylinder Will Always Stop Fully Retracted
Start Valve
Symbol Format

## Slide 43
Air Logic “MEMORY” Element
“MEMORY” Element
These elements are Normally Closed detented double pilot operated 3-Way directional valves that pass or exhaust a Supply or Input
The element Output remains (MEMORY) even when the last Signal is lost. A Signal shifts the valve to its new position but does not need to be maintained.
A Signal to the Set and Reset ports at the same time Resets the valve to its Normally Closed position.
ISO 1219–1 Symbol
Cutaway
Output
Output
S Exhaust R Supply
ANSI B93-38 1976 Symbol
S R
Supply or Input
Set
Reset
S R
S R Exhaust Supply Output
S R Exhaust Supply Output
S R Exhaust Supply Output
Set and Reset equals a Reset condition. Reset alone also equals a reset condition

## Slide 44
Air Logic “FLIP-FLOP” Element
“FLIP-FLOP” Element
These elements are detented double pilot operated 4-Way directional valves that shift an Input to an opposite Output from a momentary Set or Reset signal
They function the same as a MEMORY element except in a 4-Way configuration but they do not have differential area pilots.
Some manufacturers offer the Manual Overrides for trouble shooting ease.
ISO 1219–1 Symbol
Cutaway
Outputs
Outputs
Set Reset
ANSI B93-38 1976 Symbol
Supply or Input
Set
Reset
Reset
Set
Inlet or Supply
Outputs
Exhaust
Manual Override
Set Reset
Set Reset

## Slide 45
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element At Rest Air On
A FLIP-FLOP (F-F) in a circuit gives a positive signal and maintains it until the action starts. They also eliminate opposing signals in circuits when an actuator extends and then immediately retracts.
It replaces and is much more reliable than the ONE SHOT timer circuit shown starting at slide 78.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 46
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element Both Palm Buttons Depressed CYLA Extending
Momentarily depressing both Palm Buttons simultaneously sends a start signal to the Anti-Tie Down Unit and to F-F port 4. The F-F shifts and sends a start signal to CYLA directional valve and to LVA1 that will start CYLB after CYLA extends fully.
Shifting the F-F dropped the retract signal to CYLA and B.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 47
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Extending
CYLA continues to extend until it contacts LVA1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 48
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Extending
CYLA continues to extend until it contacts LVA1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 49
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLA continues to extend until it contacts LVA1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 50
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
When CYLA contacts LVA1 It sends a signal to extend CYLB.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 51
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 52
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 53
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 54
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 55
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 56
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 57
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 58
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 59
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 60
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 61
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Extending
CYLB continues to extend until it contacts LVB1
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 62
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
When CYLB contacts LVB1 pilot air is directed to F-F port 2 to shift it and give an output at port 3. Pilot air from port 3 shifts CYLB directional valve to start it retracting. Pilot air is also sent to LVB0 so it can retract CYLA when CYLB is fully retracted.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 63
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 64
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 65
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 66
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 67
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 68
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 69
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 70
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 71
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 72
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 73
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLB continues to retract until it contacts LVB0 and sends a signal to retract CYLA.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 74
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
When CYLB retracts fully it contacts and shifts LVB0 which sends a pilot signal to shift the directional valve that controls CYLA. CYLA directional valve shifts to retract it to its home position.
LVA1 returns to its home position as CYLA retracts.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 75
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLA continues to retract until it returns to its home position.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 76
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLA continues to retract until it returns to its home position.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 77
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLA continues to retract until it returns to its home position.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 78
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
CYLA continues to retract until it returns to its home position.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 79
Air Logic “FLIP-FLOP” Element
Typical Circuit For a “FLIP-FLOP” Element Circuit at End of Cycle At Rest
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
When CYLA fully retracts the machine is ready for another cycle.
Notice how the FLIP-FLOP supplied pilot air to shift directional valves and also dropped unwanted pilot signals at the same time.
The ONE-SHOT element in slides 82-116 is another though less reliable way to eliminate unwanted signals in this type circuit.
1
2
3
5
4
5
3
2
4
1
1
2
3
4
5

## Slide 80
Air Logic “ONE-SHOT” Element
“DIFFERENTIATOR” Element Input Air Just Turned On
A “ONE SHOT” element is a Normally Open 3-Way valve with an Accumulator Tank and either a Fixed or variable orifice to delay shifting time.
When a Signal or Input is received it immediately passes to the Output to Signal the next function. This same Input goes through an Orifice and on to an Accumulator Tank in front of the diaphragm that shifts the poppet.
When the Accumulator Tank---
ISO 1219–1 Symbol
Cutaway
Output
Input Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Output
Exhaust
Fixed Orifice Bypass Check
Accumulator Tank
Exhaust
Input

## Slide 81
Air Logic “ONE-SHOT” Element
“DIFFERENTIATIOR” Element Accumulator Tank Filled and Valve Shifted
When the Accumulator Tank fills to sufficient pressure the diaphragm shifts the poppet and stops Input air flow. After the poppet shifts air in the Output port is Exhausted to atmosphere.
The valve remains in this condition until the Input is shut off and exhausted. Inlet pressure must drop approximately 90% before the valve shifts back to the at rest condition.
ISO 1219–1 Symbol
Cutaway
Output
Input Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Output
Exhaust
Fixed Orifice Bypass Check
Exhaust
Input

## Slide 82
Air Logic “ONE-SHOT” Element
“DIFFERENTIATIOR” Element Input Shut Off and Exhausting
The poppet stays in the closed position while Input air is Exhausting until pressure drops approximately 90%. This makes sure there is no Output until the next cycle.
When the Accumulator Tank empties---
ISO 1219–1 Symbol
Cutaway
Output
Input Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Output
Exhaust
Fixed Orifice Bypass Check
Exhaust
Input

## Slide 83
Air Logic “ONE-SHOT” Element
“DIFFERENTIATIOR” Element Input Air Off Ready For Next Cycle
When the Accumulator Tank empties the poppet shifts open ready for the next Output pulse.
Fixed time “ONE SHOTS” usually have an Output duration of less than 1 second.
Adjustable “ONE SHOTS” may go as long as 2-3 minutes using external accumulators or other designs.
ISO 1219–1 Symbol
Cutaway
Output
Input Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Output
Exhaust
Fixed Orifice Bypass Check
Accumulator Tank
Exhaust
Input

## Slide 84
Simple Limit Valve Circuit
A designer may produce a circuit like the one shown here, buy the parts, install them, then hit the palm buttons and discover---
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
LVA1
LVB1
LVB0
Anti-Tie Down Unit
How a Novice Might Design a Two Cylinder Circuit At Rest Air On

## Slide 85
Simple Limit Valve Circuit
then hit the palm buttons and discover there is no movement of CYLA.
What is the problem? A check of the valve that cycles CYLA shows it has opposing signals. The first opposing signal always takes precedence so what can be done. Someone tells him about
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
LVA1
LVB1
LVB0
Anti-Tie Down Unit
How a Novice Might Design a Two Cylinder Circuit CYLA Extending

## Slide 86
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Extending
Someone tells him about a ONE-SHOT valve that will solve his problem so he installs one in the line between LVB0 and CYLA’s directional valve.
Now CYLA extends as planned --
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2

## Slide 87
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Extending
Now CYLA extends as planned.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2

## Slide 88
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
Now CYLA extends as planned.

## Slide 89
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
Now CYLA extends as planned.

## Slide 90
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
Now CYLA extends as planned, makes LVA1 which sends a signal to extend CYLB. As CYLB leaves LVB0 the ONE-SHOT exhaust rapidly as its input is dropped. It quickly returns too its normally open condition ready for another input and ONE-SHOT output.
CYLB continues to extend until it makes LVB1---
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2

## Slide 91
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 92
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 93
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 94
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1--

## Slide 95
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 96
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 97
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 98
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 99
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 100
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1---

## Slide 101
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB At End of Stroke
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
CYLB continues to extend until it makes LVB1 which should make it retract but it runs into the same opposing signals problem as CYLA did when it tried to extend,. Another ONE-SHOT saves---

## Slide 102
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
Another ONE-SHOT saves the day by getting rid of the signal from LVA1 and the cycle continues.
CYLB continues to retract until---
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 103
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 104
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 105
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 106
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 107
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 108
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 109
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 110
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 111
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 112
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4
CYLB continues to retract until---

## Slide 113
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Retracting
When CYLB fully retracts LVB0 sends pilot air to port 1 of the first ONE-SHOT and on to shift the directional valve that controls CYLA.
CYLA immediately starts retracting to its home position. As it leaves LVA1 the second ONE-SHOT starts resetting---
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 114
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Retracting
As CYLA leaves LVA1 the second ONE-SHOT exhaust rapidly as its input is dropped. It quickly returns too its normally open condition ready for another input and ONE-SHOT output.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 115
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Retracting
CYLA immediately starts retracting to its home position. As it leaves LVA1 the second ONE-SHOT starts resetting and the first ONE-SHOT times out and drops the pilot signal to CYLA’s directional valve.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 116
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Retracting
CYLA immediately starts retracting to its home position. As it leaves LVA1 the second ONE-SHOT starts resetting and the first ONE-SHOT times out and drops the pilot signal to CYLA’s directional valve.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 117
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Retracting
CYLA immediately starts retracting to its home position. As it leaves LVA1 the second ONE-SHOT starts resetting and the first ONE-SHOT times out and drops the pilot signal to CYLA’s directional valve.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 118
Simple Limit Valve Circuit
How a Novice Might Design a Two Cylinder Circuit CYLA Retracting
A ONE-SHOT valve can eliminate unwanted signals and allow a circuit to cycle. However, the length of time the signal is on is limited and may not be ample to shift sluggish valves trying to start after setting for a weekend.
The FLIP-FLOP circuit in slides 43-77 is best to use.
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
1
1
2
2
3
4
3
4

## Slide 119
Air Logic “OFF DELAY TIMER” Element
“NORMALLY OPEN TIME DELAY” Element Signal Just Received at Input
An “OFF DELAY TIMER” stops and exhaust’s a passing Supply or Signal after a predetermined time.
They may be Fixed or Variable time delays from .5 seconds up to 2-3 minutes.
They are made from a “NOT” element with an Accumulator Tank and orifice or flow control.
ISO 1219–1 Symbol
Cutaway
Input Supply Output
Output
Exhaust
Bypass Check
Accumulator Tank
Exhaust
Input Supply
Variable Adjustment
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed

## Slide 120
Air Logic “OFF DELAY TIMER” Element
“NORMALLY OPEN TIME DELAY” Element Valve Timed Out Input or Signal ON
After the valve times out the poppet shifts to block Supply or Signal and Exhaust the Output to atmosphere. It will remain in this state until the Input or Signal is removed,
After the Input is cut off the valve will---
ISO 1219–1 Symbol
Cutaway
Input Supply Output
Output
Exhaust
Bypass Check
Accumulator Tank
Exhaust
Input Supply
Variable Adjustment
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed

## Slide 121
Air Logic “OFF DELAY TIMER” Element
“NORMALLY OPEN TIME DELAY” Element Input or Signal OFF With Valve Returning to Normal
After the Input is cut off the Input bleeds off quickly through the Bypass Check and takes pressure off the diaphragm. This allows the poppet to return to the Normally Open---
ISO 1219–1 Symbol
Cutaway
Input Supply Output
Output
Exhaust
Bypass Check
Accumulator Tank
Exhaust
Input Supply
Variable Adjustment
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed

## Slide 122
Air Logic “OFF DELAY TIMER” Element
“NORMALLY OPEN TIME DELAY” Element Valve At Rest
ISO 1219–1 Symbol
Cutaway
Input Supply Output
Output
Exhaust
Bypass Check
Accumulator Tank
Exhaust
Input Supply
Variable Adjustment
After the Input is cut off the Accumulator Tank bleeds off quickly through the Bypass Check and takes pressure off the diaphragm. This allows the poppet to return to the Normally Open condition and let any Supply or Signal pass.
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed

## Slide 123
Air Logic “ON DELAY TIMER” Element
“NORMALLY CLOSED TIME DELAY” Element Signal Just Received at Input
An “ON DELAY TIMER” allows a blocked Supply or Signal to pass after a predetermined time.
They may be Fixed or Variable time delays from .5 seconds up to 2-3 minutes.
They are made from a “YES” or active “AND” element with an Accumulator Tank and orifice or flow control.
ISO 1219–1 Symbol
Cutaway
Output
Input Supply Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed
Output
Exhaust
Bypass Check
Accumulator Tank
Exhaust
Input Supply
Variable Adjustment

## Slide 124
Air Logic “ON DELAY TIMER” Element
“NORMALLY CLOSED TIME DELAY” Element Valve Timed Out Input or Signal ON
After the valve times out the poppet shifts to open Supply or Signal and block the Exhaust port. It will remain in this state until the Input or Signal is removed,
After the Input is cut off the valve will---
ISO 1219–1 Symbol
Cutaway
Input Supply Output
Output
Exhaust
Bypass Check
Exhaust
Input Supply
Variable Adjustment
Accumulator Tank
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed

## Slide 125
Air Logic “OFF DELAY TIMER” Element
“NORMALLY OPEN TIME DELAY” Element Input or Signal OFF With Valve Returning to Normal
ISO 1219–1 Symbol
Cutaway
Input Supply Output
Exhaust
Bypass Check
Accumulator Tank
Exhaust
Input Supply
Variable Adjustment
After the Input is cut off it bleeds off quickly through the Bypass Check and takes pressure off the diaphragm. This allows the poppet to return to the Normally Closed---
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed
Output

## Slide 126
Air Logic “OFF DELAY TIMER” Element
“NORMALLY OPEN TIME DELAY” Element Valve At Rest Exhausting
ISO 1219–1 Symbol
Cutaway
Output
Input Supply Output
Output
Exhaust
Bypass Check
Input Supply
Variable Adjustment
Exhaust
Accumulator Tank
After the Input is cut off the Input bleeds off quickly through the Bypass Check and takes pressure off the diaphragm. This allows the poppet to return to the Normally Closed condition and Exhaust the Output to atmosphere.
Output
ANSI B93-38 1976 Symbol
Signal In
Variable
Supply
Fixed

## Slide 127
Air Logic “FREQUENCY GENERATOR” Element
“OSCILATING” Element Just Received Input Signal
ISO 1219–1 Symbol
Cutaway
Output
Output Input
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Exhaust
Input
Exhaust
Output
Variable Adjustment
A “FREQUENCY GENERATOR” gives an Output when it receives a Signal or Input for a preset or adjustable time.
After it times out---
Accumulator Tank

## Slide 128
Air Logic “FREQUENCY GENERATOR” Element
“OSCILATING” Element Timed Out Exhausting Accumulator Tank
ISO 1219–1 Symbol
Cutaway
Output
Output Input
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Exhaust
Input
Exhaust
Output
Variable Adjustment
After it times out it shifts the poppet to the closed position and quickly Exhaust’s the Output to atmosphere.
Air trapped in the Accumulator Tank is discharged slowly and takes approximately twice as long to exhaust as it took to fill.
When the Accumulator Tank empties to approximately 10% of its shifting pressure---
Accumulator Tank

## Slide 129
Air Logic “FREQUENCY GENERATOR” Element
“OSCILATING” Element Resetting For Another Output
ISO 1219–1 Symbol
Cutaway
Output
Output Input
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Exhaust
Input
Exhaust
Output
Variable Adjustment
When the Accumulator Tank empties to approximately 10% of its shifting pressure the poppet shifts back to the open position and gives another timed Output signal.
This action repeats---
Accumulator Tank

## Slide 130
Air Logic “FREQUENCY GENERATOR” Element
“OSCILATING” Element Giving a Repeat Signal
ISO 1219–1 Symbol
Cutaway
Output
Output Input
ANSI B93-38 1976 Symbol
Signal In
Variable
Fixed
Exhaust
Input
Exhaust
Output
Variable Adjustment
Accumulator Tank
This action repeats as long as there is an Input.

## Slide 131
Other Available Logic Elements
These Are All Manufacturers Catalog Symbols
Normally Closed Normally Open
Amplifier Element that takes a very low pressure signal and amplifies it to system pressure.
Anti Tie Down unit that requires two inputs within .5– 1 second of one another to produce an output (See Slides 129-147 for Internal Logic)
Output
Normally Closed Normally Open Normally Closed Normally Open
Gives or drops an Output after receiving a an adjustable pressure Signal of positive or negative pressure. Normally used to indicate pressure or vacuum amount before starting next operation. Use with caution since pressure buildup can come for any reason not necessarily end of stroke position.
Signal
Output
Signal
Output

## Slide 132
Other Available Logic Elements
These Are All Manufacturers Catalog Symbols
Air operated Venturi that produces low volume Vacuum from pressurized air.
Vacuum Cups to pick up and/or hold production parts.
Pre-Select Counter with manual reset. Counts input signals and gives an Output after a predetermined number of Inputs. After Reset it repeats count cycle again.
Positive Input
Vacuum
Vacuum
Indicators in Red, Blue, Green or Yellow. Appear clear until air is applied then change color to show function activated.
0 0 0 0 0
0 0 0 2 6
0 0 0 0 0 0
Count Signal
Supply
Output
Reset
Count Signal
Part or cycle counter to keep a running total of number made since last manual reset.

## Slide 133
Other Available Logic Elements
Solenoid operated valves to change an electrical input to an air output.
Signal
Pressure activated switch to send or break an electric output to a PLC, other controller or device.
Normally Closed
Normally Closed
Normally Open
Inline “AND Element Inline “OR” Element

## Slide 134
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Air Logic Symbol Format At Rest Air On
OR
AND
NOT 1
NOT 2
.5 Second TIME ON Delay
Air In

## Slide 135
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format At Rest Air On
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
Air In

## Slide 136
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Only One Palm Button Depressed
OR
AND
.5 Second TIME ON Delay
If one Palm Button is pressed and held for more that .5 seconds the Time On Delay---
NOT 2
NOT 1
Air In

## Slide 137
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Only One Palm Button Depressed
OR
AND
NOT 2
NOT 1
.5 Second TIME ON Delay
If one Palm Button is pressed and held for more that .5 seconds the TIME ON Delay times out and shifts NOT1 closed. This blocks the AND output---.
Air In

## Slide 138
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Depressing Second Palm Button After Time Delay Has Timed Out
OR
AND
NOT 2
NOT 1
.5 Second TIME ON Delay
This blocks the AND output even if the second Palm Button is depressed. This keeps an operator from locking one valve down and cycling the machine one handed.
Air In

## Slide 139
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Depressing Both Palm Buttons Concurrently (Simultaneously)
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
Depressing both Palm Buttons at the same time immediately sends a Signal to shift the directional valve and start the cylinder extending. At the same time the TIME ON delay starts timing and will time---
Air In

## Slide 140
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Depressing Both Palm Buttons Concurrently (Simultaneously)
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
At the same time the TIME ON delay starts timing and will time out before the cycle completes. However, NOT 2 is being held closed at this time blocking the Signal from the timer. If the operator lets up either---
Air In

## Slide 141
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format One Palm Button Released During Cycle Cylinder Retracting
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
If the operator lets up either Palm Button and opens the possibility of a Safety Hazard the circuit will immediately reverse cylinder action since the AND output is lost. This also drops the signal to NOT 2 ---
Air In

## Slide 142
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Cylinder Retracting, AND Output Blocked at NOT 1
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
This also drops the Signal to NOT 2, it shifts and sends a blocking Signal to NOT 1. Now both Palm Buttons must be released to allow the timer to reset and drop its output before another cycle can start.
Air In

## Slide 143
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In ISO Symbol Format Ready For Another Cycle
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
Air In

## Slide 144
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format At Rest Air On
OR
AND
NOT 2
NOT 1
.5 Second TIME ON Delay
Air In

## Slide 145
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Only One Palm Button Depressed
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
If one Palm Button is pressed and held for more that .5 seconds the Time On Delay will---
Air In

## Slide 146
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Only One Palm Button Depressed
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
If one Palm Button is pressed and held for more that .5 seconds the TIME ON Delay times out and shifts NOT1 closed. This blocks the AND output---.
Air In

## Slide 147
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Depressing Second Palm Button After Time Delay Has Timed Out
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
This blocks the AND output even if the second Palm Button is depressed. This keeps an operator from locking one valve down and cycling the machine one handed.
Air In

## Slide 148
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Depressing Both Palm Buttons Concurrently (Simultaneously)
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
Depressing both Palm Buttons at the same time immediately sends a Signal to shift the directional valve and start the cylinder extending. At the same time the TIME ON delay starts timing and will time---
Air In

## Slide 149
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Depressing Both Palm Buttons Concurrently (Simultaneously)
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
At the same time the TIME ON delay starts timing and will time out before the cycle completes. However, NOT 2 is being held closed at this time blocking the Signal from the timer. If the operator lets up either---
Air In

## Slide 150
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format One Palm Button Released During Cycle Cylinder Retracting
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
If the operator lets up either Palm Button and opens the possibility of a Safety Hazard the circuit will immediately reverse cylinder action since the AND output is lost. This also drops the signal to NOT 2 ---
Air In

## Slide 151
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Cylinder Retracting, AND Output Blocked at NOT 1
OR
AND
.5 Second TIME ON Delay
NOT 2
NOT 1
This also drops the Signal to NOT 2, it shifts and sends a blocking Signal to NOT 1. Now both Palm Buttons must be released to allow the timer to reset and drop its output before another cycle can start.
Air In

## Slide 152
Simple Anti-Tie Down Circuit
Anti-Tie Down Safety Circuit In Cutaway Format Ready For Another Cycle
OR
AND
NOT 2
NOT 1
.5 Second TIME ON Delay
Air In

## Slide 153
Air Logic “SEQUENCER” Element
Programmable “Sequencer” Element Symbol Format
Manufacturers Symbol
Supply
Output
Reset
ANSI B93-38 1976 Symbol ISO 1219–1 Symbol
Output Input
Set
Set
Reset
Set
Set
Output Input
Supply
Reset
Reset
Input

## Slide 154
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit At Rest Air On
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Input LVA1
Manufacturers Symbol
Input
Output
Output A-
Input LVA0
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR

## Slide 155
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit Cycle Start CYLA Extending
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Input LVA1
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0

## Slide 156
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit CYLA Fully Extended Contacting LVA1
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Input LVA1
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0

## Slide 157
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit CYLA Starting to Retract
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Input LVA1
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0

## Slide 158
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit CYLA Retracting
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0
Input LVA1

## Slide 159
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit CYLA Fully Retracted Contacting LVA0
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0
Input LVA1

## Slide 160
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit CYLA Fully Retracted
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0
Input LVA1

## Slide 161
Air Logic “SEQUENCER” Assembly
Programmable “Sequencer” Circuit At Rest Air On
Supply
Reset
Set or Start
Cycle in Progress
Set
Supply
Output A+
Manufacturers Symbol
Input
Output
Output A-
Memory
AND or other module such as a TIME DELAY to modify start of next Sequencer
OR
Input LVA0
Input LVA1

## Slide 162
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit At Rest Air On
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
Sequencer circuits are simple to design even when they include immediate reversing of actuators. All that is required is a Sequence of Events to determine the number of Sequencers and what other devices such as AND and OR’s might be necessary.
From CYLA rod end line for anti-repeat capability

## Slide 163
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Both Palm Buttons Depressed CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
Depressing both Palm Buttons at the same time sends a signal through through Anti Tie Down Unit to the Sequencer start Input and immediately gives an A+ Output. CYLA starts extending and leaves LVA0 and exhaust’s its Output to atmosphere.
A+ Output stays on---
From CYLA rod end line for anti-repeat capability

## Slide 164
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Both Palm Buttons Depressed CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
A+ Output stays on for the complete extend stroke of CYLA so even if the valve is slow in shifting it will always shift if possible.
CYLA continues extending until it --
From CYLA rod end line for anti-repeat capability

## Slide 165
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Both Palm Buttons Depressed CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLA continues extending until it makes LVA1.
From CYLA rod end line for anti-repeat capability

## Slide 166
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Both Palm Buttons Depressed CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLA continues extending until it makes LVA1.
From CYLA rod end line for anti-repeat capability

## Slide 167
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Both Palm Buttons Depressed CYLA Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
When CYLA fully extends it shifts LVA1 and sends a signal to the first Sequencer Module to show the action is complete and cause the second Sequencer Module to give Output B+.
CYLB starts extending as the second part of the sequence.
From CYLA rod end line for anti-repeat capability

## Slide 168
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Both Palm Buttons Depressed CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLB starts extending as the second part of the sequence.
A+ signal is dropped even though LVA1 is still made. The Output of LVA1 is blocked by an AND element in the Sequencer Module.
Input pressure to the right Palm Button is lost when CYLA is fully extended so the Anti-Tie Down unit loses its Output even if the valves are held shifted.
From CYLA rod end line for anti-repeat capability

## Slide 169
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLB continues extending until it --
From CYLA rod end line for anti-repeat capability

## Slide 170
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLB continues extending until it --
From CYLA rod end line for anti-repeat capability

## Slide 171
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLB continues extending until it --
From CYLA rod end line for anti-repeat capability

## Slide 172
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB1
LVB0
LVA0
LVA1 LVA0 LVB1 LVB0
A+ B+ B- B+ B- A-
A+
A-
B+
B-
CYLB continues extending until it makes LVB1 which sends a signal to the second Sequencer Module to tell it the cylinder has completed its stroke. At the same time it causes the third Sequencer Module to send a signal to retract CYLB.
From CYLA rod end line for anti-repeat capability

## Slide 173
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB0
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues retracting until it makes---.
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-

## Slide 174
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB0
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues retracting until it makes---.
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-

## Slide 175
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB0
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues retracting until it makes---.
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-

## Slide 176
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB0
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues retracting until it makes---.
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-

## Slide 177
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB0
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues retracting until it makes---.
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-

## Slide 178
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVB0
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues retracting until it makes LVB0 which sends a signal to third Sequencer Module to tell it the cylinder has completed its stroke. It also drops out B- and sends a B+ signal to start extending CYLB again.
CYLB continues extending until---
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-

## Slide 179
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues extending until---
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-
LVB0

## Slide 180
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues extending until---
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-
LVB0

## Slide 181
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+ B+ B- B+ B- A-
A+
A-
CYLB continues extending until---
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-
LVB0

## Slide 182
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+ B+ B- B+ B- A-
A+
A-
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-
LVB0
CYLB continues extending until---

## Slide 183
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Extending
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+ B+ B- B+ B- A-
A+
A-
From CYLA rod end line for anti-repeat capability
LVB1
B+
B-
LVB0
CYLB continues extending until---

## Slide 184
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
CYLB continues extending until it makes LVB1 and signals Sequencer Module five to start it retracting again.
CYLB immediately starts to retract for the second time and continues on until---
LVB1

## Slide 185
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
CYLB immediately starts to retract for the second time and continues on until---

## Slide 186
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
CYLB immediately starts to retract for the second time and continues on until---

## Slide 187
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
CYLB immediately starts to retract for the second time and continues on until---

## Slide 188
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
CYLB immediately starts to retract for the second time and continues on until---

## Slide 189
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLB Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
CYLB immediately starts to retract for the second time and continues on until---

## Slide 190
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA1
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
CYLB immediately starts to retract for the second time and continues on until it makes LVB0 and gives Sequencer Module five an end of stroke signal and signals Sequencer Module six to retract CYLA.
CYLA continues to retract---
LVB0

## Slide 191
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
LVA1
CYLA continues to retract---

## Slide 192
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
LVA1
CYLA continues to retract---

## Slide 193
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
LVA0
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
LVA1
CYLA continues to retract---

## Slide 194
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit CYLA Retracting
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
LVA1
CYLA continues to retract until it makes LVA0 which signals Sequencer Module six the cycle is finished.
Cycle finish resets all Sequencers to off---
LVA0

## Slide 195
A+ B+ B- B+ B- A-
LVA1 LVA0 LVB1 LVB0
Air Logic “SEQUENCER” Circuit
Programmable “Sequencer” Circuit Ready For A New Cycle
CYLA
CYLB
Cycle Sequence: CYLA Extend A+ CYLB Extend B+ CYLB Retract B- CYLB Extend B+ CYLB Retract B- CYLA Retract A-
Anti-Tie Down Unit
A+
A-
From CYLA rod end line for anti-repeat capability
B+
B-
LVB0
LVA1
Cycle finish resets all Sequencers to off position and the Cycle in Progress indicator goes off.
LVA0

## Slide 196: “Fluid Power Circuits Explained”
This information was taken from
“Fluid Power Circuits Explained”
It covers these components and other circuits commonly used in industry
Learn about the ways Air Logic Controls can replace expensive electrical controls in some applications

## Slide 197: For More Information on Air Logic Controls and Many Other Fluid Power Circuits See “Fluid Power Circuits Explained” by the Author of this Presentation
Table of Contents from “Fluid Power Circuits Explained”
1. Accumulator Circuits 13. Intensifier Circuits
2. Air Logic Valve Circuits 14. Proportional Control Valve Circuits
3. Air-Oil Circuits 15. Pump Circuits
4. Cartridge Valve Circuits 16. Reducing Valve Circuits
5. Counter Balance Valve Circuits 17. Regeneration Circuits
6. Cylinder Circuits 18. Relief Valve Circuits
7. Decompression Circuits 19. Rotary Actuator Circuits
8. Directional Control Valve Circuits 20. Sequence Valve Circuits
9. Filter Circuits 21. Servo Control Valve Circuits
10. Flow Control Circuits 22. Synchronizing Circuits
11. Flow Divider Circuits 23. Sample Actual Circuits
12. Fluid Motor Circuits

## Slide 198: “Fluid Power Circuits Explained”
The book is in schematic format so you need to be familiar with Fluid Power symbols to understand the circuits.
· The book contains 375 pages of basic pneumatic and hydraulic circuits shown in schematic form with an explanation of their function. It is in a convenient 3-ring binder format.
· There are 22 sections covering Accumulators, Air Logics, Air-Oil Systems, Cartridge valves, Counter Balance Valves Cylinders, De-Compression, Directional Controls, Filters, Flow Dividers, Intensifiers, Proportional Valves, Pumps, Reducing Valves, Regeneration, Relief Valves, Rotary Actuators, Sequence Valves, Servo Controls and Synchronizing Circuits. There is also a section with some actual operating circuits with explanations.
· Most circuits show what happens when the valves and actuators cycle. A detailed explanation of the schematic explains cycle progress and possible problem areas.
List price is $105.00 plus $7.95 S&H for shipments in the continental U.S. All other countries will be billed actual postage/shipping cost for the requested method. Indiana residents add 5% Sales Tax.
Send a check or money order to: HYDRA-PNEU CONSULTING, INC.
726 Outer Gray Street
Newburgh, IN 47630-1517